Florida Supplement to the 2012 IMC

POST-GLITCH CORRECTION VERSION

Note 1:  Throughout the document, change International Building Code to Florida Building Code, Building; change the ICC Electrical Code to Chapter 27 of the Florida Building Code, Building; change the International Energy Conservation Code to the Florida Building Code, Energy Conservation; change the International Existing Building Code to Florida Building Code, Existing Building; change the International Fire code to Florida Fire Prevention Code; change International Fuel Gas Code to Florida Building Code, Fuel Gas; change the International Mechanical Code to Florida Building Code, Mechanical; change the International Plumbing Code to Florida Building Code, Plumbing; change the International Residential Code to Florida Building Code, Residential.

Note 2:  Criteria blocked in yellow indicate Florida specific language from the 2010 FBC.

PREFACE

Introduction

Development

History

The State of Florida first mandated statewide building codes during the 1970s at the beginning of the modern construction boom. The first law required all municipalities and counties to adopt and enforce one of the four state-recognized model codes known as the “state minimum building codes.” During the early 1990s a series of natural disasters, together with the increasing complexity of building construction regulation in vastly changed markets, led to a comprehensive review of the state building code system. The study revealed that building code adoption and enforcement was inconsistent throughout the state and those local codes thought to be the strongest proved inadequate when tested by major hurricane events. The consequences of the building codes system failure were devastation to lives and economies and a statewide property insurance crisis. The response was a reform of the state building construction regulatory system that placed emphasis on uniformity and accountability.

The 1998 Florida Legislature amended Chapter 553, Florida Statutes (FS), Building Construction Standards, to create a single state building code that is enforced by local governments. As of March 1, 2002, the Florida Building Code, which is developed and maintained by the Florida Building Commission, supersedes all local building codes. The Florida Building Code is updated every three years and may be amended annually to incorporate interpretations and clarifications.

Scope

The Florida Building Code is based on national model building codes and national consensus standards which are amended where necessary for Florida’s specific needs. However, code requirements that address snow loads and earthquake protection are pervasive; they are left in place but should not be utilized or enforced because Florida has no snow load or earthquake threat.  The code incorporates all building construction-related regulations for public and private buildings in the State of Florida other than those specifically exempted by Section 553.73, Florida Statutes. It has been harmonized with the Florida Fire Prevention Code, which is developed and maintained by the Department of Financial Services, Office of the State Fire Marshal, to establish unified and consistent standards.

The base codes for the Fifth edition (2014)  of the Florida Building Code include: the International Building Code®, 2012 edition; the International Plumbing Code®, 2012 edition; the International Mechanical Code®, 2012 edition; the International Fuel Gas Code®, 2012 edition; the International Residential Code®, 2012 edition; the International Existing Building Code®, 2012 edition; the International Energy Conservation Code, 2012; the National Electrical Code, 2011 edition; substantive criteria from the American Society of Heating, Refrigerating and Air-conditioning Engineers’ (ASHRAE) Standard 90.1-2010. State and local codes adopted and incorporated into the code include the Florida Building Code, Accessibility, and special hurricane protection standards for the High-Velocity Hurricane Zone.

The code is composed of nine main volumes: the Florida Building Code, Building, which also includes state regulations for licensed facilities; the Florida Building Code, Plumbing; the Florida Building Code, Mechanical; the Florida Building Code, Fuel Gas; the Florida Building Code, Existing Building; the Florida Building Code, Residential; the Florida Building Code, Energy Conservation; the Florida Building Code, Accessibility and the Florida Building Code, Test Protocols for High-Velocity Hurricane Zones. Chapter 27 of the Florida Building Code, Building, adopts the National Electrical Code, NFPA 70, by reference.

Under certain strictly defined conditions, local governments may amend requirements to be more stringent than the code. All local amendments to the Florida Building Code must be adopted by local ordinance and reported to the Florida Building Commission then posted on www.floridabuilding.org  in Legislative format for a month before being enforced. Local amendments to the Florida Building Code and the Florida Fire Prevention Code may be obtained from the Florida Building Commission web site, or from the Florida Department of Business and Professional Regulation or the Florida Department of Financial Services, Office of the State Fire Marshal, respectively.

Adoption and Maintenance

[Note to editor:  Replace ICC “Adoption” and “Maintenance” with the following text:]

The Florida Building Code is adopted and updated with new editions triennially by the Florida Building Commission. It is amended annually to incorporate interpretations, clarifications and to update standards. Minimum requirements for permitting, plans review and inspections are established by the code, and local jurisdictions may adopt additional administrative requirements that are more stringent. Local technical amendments are subject to strict criteria established by Section 553.73, F.S. They are subject to Commission review and adoption into the code or repeal when the code is updated triennially and are subject to appeal to the Commission according to the procedures established by Section 553.73, F.S.

Eleven Technical Advisory Committees (TACs), which are constituted consistent with American National Standards Institute (ANSI) Guidelines, review proposed code changes and clarifications of the code and make recommendations to the Commission. These TACs whose membership is constituted consistent with American National Standards Institute (ANSI) Guidelines include: Accessibility; Joint Building Fire (a joint committee of the Commission and the State Fire Marshal); Building Structural; Code Administration/ Enforcement; Electrical; Energy; Mechanical; Plumbing and Fuel Gas; Roofing; Swimming Pool; and Special Occupancy (state agency construction and facility licensing regulations).

The Commission may only issue official code clarifications using procedures of Chapter 120, Florida Statutes. To obtain such a clarification, a request for a Declaratory Statement (DEC) must be made to the Florida Building Commission in a manner that establishes a clear set of facts and circumstances and identifies the section of the code in question. Requests are analyzed by staff, reviewed by the appropriate Technical Advisory Committee, and sent to the Florida Building Commission for action. These interpretations establish precedents for situations having similar facts and circumstances and are typically incorporated into the code in the next code amendment cycle. Non-binding opinions are available from the Building Officials Association of Florida’s web site (www.BOAF.net) and a Binding Opinion process is available online at www.floridabuilding.org.

Code Development Committee Responsibilities (Letter Designations in Front of Section Numbers)

[Note to editor:  Use paragraphs 1 and 2 specific to this code through the code committee descriptors.  Delete the remaining text in this section.]

Marginal Markings

Solid vertical lines in the margins within the body of the code indicate a technical change from the requirements of the 2009 edition. Deletion indicators in the form of an arrow (→) are provided in the margin where an entire section, paragraph, exception or table has been deleted or an item in a list of items or table has been deleted.

Dotted vertical lines in the margins within the body of the supplement indicate a change from the requirements of the base codes to the 2014 Florida Building Code effective TBD

Sections deleted from the base code are designated “Reserved”  in order to maintain the structure of the base code.

Italicized Terms

[No change to I Code text.]

Acknowledgments

The Florida Building Code is produced through the efforts and contributions of building designers, contractors, product manufacturers, regulators and other interested parties who participate in the Florida Building Commission’s consensus processes, Commission staff and the participants in the national model code development processes.

[Note to Editor:    Delete the following ICC text in its entirety:]

Effective Use of the …

Legislation

Chapter 1, Administration

Section 101 General

101.1 Scope. Change to read as shown.

[A] 101.1 Title. These regulations shall be known as the Mechanical Code of [NAME OF JURISDICTION], hereinafter referred to as "this code.”  Scope. The provisions of Chapter 1, Florida Building Code, Building shall govern the administration and enforcement of the Florida Building Code, Mechanical.

101.2 Scope. Change to read as shown.

101.2 Scope. Reserved.

101.3 Intent. Change to read as shown.

101.3 Intent. Reserved.

101.4    Severability. Change to read as shown.

101.4 Severability. Reserved.

Section 102 Applicability. Change to read as shown.

Section 102 Applicability. Reserved.

Section 103, Department of Mechanical Inspection. Change to read as shown.

Section 103, Department of Mechanical Inspection. Reserved.

Section 104, Duties and Powers of the Code Official. Change to read as shown.

Section 104, Duties and Powers of the Code Official. Reserved.

Section 105, Approval. Change to read as shown.

Section 105, Approval. Reserved.

Section 106, Permits. Change to read as shown.

Section 106, Permits. Reserved.

Section 107, Inspections and Testing. Change to read as shown.

Section 107, Inspections and Testing.  Reserved.

Section 108, Violations. Change to read as shown.

Section 108, Violations. Reserved.

Section 109, Means of Appeal. Change to read as shown.

Section 109, Means of Appeal. Reserved.

Section 110, Temporary Equipment, Systems and Uses. Change to read as shown:

Section 110. Temporary Equipment, Systems and Uses. Reserved.

(M5201 AS)

Chapter 2, Definitions

SECTION 202

GENERAL DEFINITIONS

Section 202 General definitions. Change definitions specified to read as follows:

BOILER, HOT WATER SUPPLY. Any vessel used for generating hot water to be used external to the vessel, which exceeds any of the following limitations:

1. A heat input capacity of 400,000 Btuh (117.2 kW).

2. A water temperature of 210ºF (99ºC).

3. A nominal water capacity of 120 gal (454 L).

(M5645 AM- A1)

DESIGN FLOOD ELEVATION. The elevation of the “design flood,” including wave height, relative to the datum specified on the community’s legally designated flood hazard map. In areas designated as Zone AO, the design flood elevation shall be the elevation of the highest existing grade of the building’s perimeter plus the depth number (in feet) specified on the flood hazard map. In areas designated as Zone AO where a depth number is not specified on the map, the depth number shall be taken as being equal to 2 feet (610 mm).

(SP5283 AS)

Chapter 3, General Regulations

SECTION 301

GENERAL

Section 301.16.1 High-velocity wave action. Change to read as follows:

301.16.1 High-velocity wave action Coastal high hazard areas. In flood hazard areas subject to high-velocity wave action coastal high hazard areas, mechanical systems and equipment shall not be mounted on or penetrate walls intended to break away under flood loads.    (SP5682 AM)(SP5679 AS)

SECTION 307

CONDENSATE DISPOSAL

Section 307.2.5. Add to read as follows:

307.2.5 Pipe insulation. All horizontal primary condensate drains within unconditioned areas shall be insulated to prevent condensation from forming on the exterior of the drain pipe.

(M5756 AS)

Chapter 5, Exhaust Systems

Section 515. Add section to read as follows:

SECTION 515

MAUSOLEUM RELIEF VENT

515.1 General. A pressure relief vent shall be provided for each crypt. Niches shall not require pressure relief systems.

515.2 Materials. The pressure relief vent pipe and fittings shall conform to one of the standards listed in Table M515.2A and Table M515.2B.

TABLE 515.2A

CRYPT PRESSURE RELIEF PIPE

MATERIAL                                     					STANDARD

Acrylonitrile butadiene styrene (ABS) plastic pipe		ASTM D 2661

ASTM F 628 CSA B181.1

Polylefin pipe	                   		                             	CSA CAN/CSA - B181.3

Polyvinyl chloride (PVC) plastic pipe  (Type DWV)	            ASTM D 2665

ASTM D 2949, ASTM F 891

Table 515.2B

CRYPT PRESSURE RELIEF FITTINGS

MATERIAL			                              	              	STANDARD

Acrylonitrile butadiene styrene (ABS) plastic pipe   		              ASTM D 3311,  CSA B181.1

Polyvinyl chloride (PVC) plastic pipe (Type DWV)     ASTM D 3311, ASTM D 2949, ASTM F 891

Plastic, general			                                                   ASTM F 409

515.3 Pressure Relief Vent.  For family mausoleum units where all crypts are bordering an exterior wall, pressure relief ventilation shall be provided from the crypt to the outside of the mausoleum through the exterior wall or roof. For all other mausoleum units, each crypt shall have a pressure relief vent from the crypt to the roof of the mausoleum. The minimum nominal pipe size shall be 1 inch (25 mm). The system shall have a minimum of one-eighth unit vertical to 12 units horizontal (1-percent slope). The piping shall not be trapped or installed to trap water or condensate.

515.4 Termination.  Except for family mausoleum units where all crypts are bordering an exterior wall, crypt pressure relief system shall extend through the roof and terminate at least 6 inches (152 mm) above the roof and at least 10 feet (3048 mm) from any openable opening, air intake, or property line. The termination of the relief system pipe shall be done by a roof and vent cap compatible with the relief pressure pipe. The roof and vent cap shall be waterproof.  For family mausoleum units where all crypts are bordering an exterior wall, pressure relief ventilation shall be provided from the crypt to the outside of the mausoleum through the exterior wall or roof.

(SP5223 AS)

Section 516. Add a section to read as follows:

SECTION 516

CARBON MONOXIDE CONTROL SYSTEMS

516.1 Carbon monoxide control systems. See Section 908.7 916 of the Florida Building Code, Building.

(M5228 AM)

Chapter 6, Duct Systems

Section 601 General. Add Section 601.5 to read as follows:

601.5 Balanced Return Air. Restricted return air occurs in buildings when returns are located in central zones and closed interior doors impede air flow to the return grill or when ceiling spaces are used as return plenums and fire walls restrict air movement from one portion of the return plenum to another. Provisions shall be made in both residential and commercial buildings to avoid unbalanced air flows and pressure differentials caused by restricted return air. Pressure differentials across closed doors where returns are centrally located shall be limited to 0.01 inch WC (2.5 pascals) or less. Pressure differentials across fire walls in ceiling space plenums shall be limited to 0.01 inch WC (2.5 pascals) by providing air duct pathways or air transfer pathways from the high pressure zone to the low zone.

Exceptions:

1.      Transfer ducts may achieve this by increasing the return transfer 1½ times the cross sectional area (square inches) of the supply duct entering the room or space it's serving and the door having at least an unrestricted 1 inch undercut to achieve proper return air balance.

2.      Transfer grilles shall use 50 square inches (of grille area) to 100 cfm (of supply air) for sizing through-the-wall transfer grilles and using an unrestricted 1 inch undercutting of doors to achieve proper return air balance.

3.      Habitable rooms only shall be required to meet these requirements for proper balanced return air excluding bathrooms, closets, storage rooms and laundry rooms, except that all supply air into the master suite shall be included.

(M5772 AM)

SECTION 603

DUCT CONSTRUCTION AND INSTALLATION

Section 603.1.1. Add section to read as follows:

603.1.1 Space provided. Sufficient space shall be provided adjacent to all mechanical components located in or forming a part of the air distribution system to assure adequate access for (1) construction and sealing in accordance with the requirements of Section 603.1 of this code; (2) inspection; and (3) cleaning and maintenance. A minimum of 4 inches (102 mm) is considered sufficient space around air handling units.

Exception: Retrofit or replacement units not part of a renovation are exempt from the minimum clearance requirement

(M5776 AS)

Chapter 10, Boilers, Water Heaters and Pressure Vessels

Add Section 1004.2.1 to read as follows:

1004.2.1  Carbon monoxide testing. Boilers shall be tested to a maximum level of 50 PPM of carbon monoxide as per OSHA guidelines.

(Post-Glitch Comment MC1 AS)

Chapter 15, Referenced Standards

Change to make Florida-specific references as follows:

ASTM

Standard										Referenced in

Reference 										code section

Number		Title									number

D 2661—01 Acrylonitrile-Butadiene-Styrene (ABS) Schedule 40 Plastic Drain, Waste, and Vent

Pipe and Fittings…………………………………………………………………………Table 515.2A

D2665—01  Poly (Vinyl Chloride) (PVC) Plastic Drain, Waste, and Vent Pipe and Fittings…………Table 515.2A

D 2949—97  3.25-in. Outside Diameter Poly (Vinyl Chloride) (PVC) Plastic Drain, Waste,

and Vent Pipe and Fittings………………………………………………………Table 515.2A, 515.2B

D 3311—94  Drain, Waste, and Vent (DWV) Plastic Pipe Fittings Patterns………………………….. Table 515.2B

F 409—02     Thermoplastic Accessible and Replaceable Plastic Tube and Tubular Fittings	    Table 515.2B

F 628—01     Acrylonitrile-Butadiene-Styrene (ABS) Schedule 40 Plastic Drain, Waste, and Vent

Pipe with Cellular Core…………………………………………………………………………………..Table 515.2A

F 891—00 Coextruded Poly (Vinyl Chloride) (PVC) Plastic Pipe with Cellular Core…..Table 515.2A, Table 515.2B

CSA

Standard										 Referenced in

Reference 										 code section

Number		        Title								  number

CAN/CSA B 181.1—99 ABS Drain, Waste, and Vent Pipe and Pipe Fittings………………..Tables 515.2A, 515.2B

CAN/CSA B 181.3—99 Polyolefin Laboratory Drainage Systems with revisions through

October 1990………………………………………………………………………Table 515.2A

Florida Codes Florida Building Commission

c/o Florida Department of Business and Professional Regulation

Building Codes and Standards

1940 North Monroe Street, Suite 90A

Tallahassee, Florida 32399-0722.

Standard                                                                                                                                          Referenced in code

reference number    Title                                                                                                                 section number

FBC-B—14 ICC-12 International Building Code  Florida Building Code, Building                         101.1, 201.3, 202, 301.12, 301.12, 301.14, 301.15, 302.1, 302.2,

304.7, 304.10, 308.8, 308.10, 401.4, 401.6, 406.1, 502.10,

502.10.1, 504.2, 506.3.3, 506.3.10, 506.3.12.2, 506.4.1, 509.1,

510.6, 510.6.3, 510.6.2, 510.7, 511.1.5, 513.1,

513.2, 513.3, 513.4.3, 513.5, 513.5.2, 513.5.2.1,

513.6.2, 513.10.5, 513.12, 513.12.2, 513.20, 516.1,

602.2.1.5.1, 602.2.1.5.2, 602.3, 603.1, 603.10,

604.5.4, 607.1.1, 607.3.2.1, 607.5.1, 607.5.2,

607.5.3, 607.5.4, 607.5.4.1, 607.5.5, 607.5.5.1,

607.6, 607.6.2, 701.4.1, 701.4.2, 801.3, 801.16.1,

801.18.4, 902.1, 908.3, 908.4, 910.3, 925.1,

1004.6, 1105.1, 1206.4, 1402.4, 1402.4.1

FBC-EC—14 ICC-12 International Energy Conservation Code Florida Building Code, Energy Conservation      202, 301.2, 303.3, 312.1, 603.9, 604.1, 1204.1, 1204.2

FBC-FG—14 ICC-12 International Fuel Gas Code Florida Building Code, Fuel Gas                               101.2, 201.3, 301.3, 701.1, 801.1, 901.1, 906.1, 1101.5

FBC-P—14 ICC-12 International Plumbing Code Florida Building Code, Plumbing	                                201.3, 301.8, 512.2, 908.5, 1002.1, 1002.2, 1002.3,

1005.2, 1006.6, 1008.2, 1009.3, 1101.4,

1201.1, 1206.2, 1206.3, 1401.2

FFPC—13 IFC-12 International Fire Code Florida Fire Prevention Code                                                	201.3, 310.1, 311.1, 502.4, 502.5, 502.7.2, 502.8.1, 502.9.5, 502.9.5.2,

502.9.5.3, 502.9.8.2, 502.9.8.3, 502.9.8.5, 502.9.8.6, 502.10,

502.10.3, 502.16.2, 509.1, 510.2.1, 510.2.2, 510.4,

511.1.1 513.12.3, 513.15, 513.16, 513.17, 513.18, 513.19,

513.20.2, 513.20.3, 606.2.1, 908.7, 1101.9,

1105.3, 1105.9, 1106.5, 1106.6, 1301.1, 1301.2

Delete all references to ICC codes in their entirety.

ICC