## Slide 1: Survey and Investigation of Corrosion of Fasteners used to Secure Roofing Systems
Draft Final Report
Submitted June 15, 2014
Forrest Masters, Kurtis Gurley
David Prevatt, Eric Burkett

## Slide 2: Summary of Report
Mark Zehnal is the point of contact
Literature review performed
Survey vendor identified and engaged
    UF Survey Research Center (UFSRC)
Survey subject contact list created through DBPR
Questionnaire finalized and administered
  385 responses from roofing contractors
Results analyzed
Discussion of the next steps

## Slide 3: Survey Vendor
UF Survey Research Center (URL in the report)
    UF affiliated vendor
    Necessary expertise
    Budget based projection ~ 240 completed surveys
    Actual production  385 completed surveys
Services
    Refine questionnaire
    Programming, testing, sample cleaning
    IRB approval
    Administer Survey
    Top-level analysis and report production

## Slide 4: Survey Subject Database
Data request filed with DBPR
  Contact information for licensed contractors, inspectors, building officials
DBPR responded quickly, resulting in
  6500 contractors  ~ 4000 with contact information
  5600 inspectors / officials  ~ 1000 with contact information

## Slide 5: Phone Survey Methodology
Conducted May 13 to May 30
1500 contacts randomly selected from list of 4000 contractors
Inspectors were not targeted due to issues with phone contact during working hours
385 surveys were completed
  25.7% response rate far exceeded typical response rate
385 responses yields ~5% margin of error

## Slide 6: Survey Results
About the 385 respondents
  88% were roofing contractors
  6.5% were roofing inspectors
  1.2% were building officials
  4.5% other
  Mean years of experience  18.9 years
  10% have worked in Miami-Dade
  85% have worked within 10 miles of the FL coast
  80% reported observing corrosion

## Slide 7: Survey Results
Response options
  Never
  Almost never
  Sometimes  sm
  Usually
  Always
  No experience
  Don’t know / refuse to answer
n/an
us/al

## Slide 8: Survey Results
% of responders who observed corrosion by system:
 | us/al | sm | n/an
Shingle fasteners | 34% | 44% | 17%
Tile fasteners | 16% | 37% | 26%
Metal roof fasteners | 28% | 39% | 22%
Ridge vent fasteners | 42% | 38% | 14%
Penetration fasteners | 24% | 45% | 25%

## Slide 9: Survey Results
% of responders who observed corrosion by coastal proximity:
 | us/al | sm | n/an
Within 10 miles of coast | 58% | 29% | 5%
Inland | 17% | 60% | 18%

## Slide 10: Survey Results
% of responders who observed corrosion by fastener type:
 | us/al | sm | n/an
Smooth nail | 35% | 46% | 12%
Ring shank | 16% | 48% | 31%
Barbed | 13% | 43% | 21%
Screw | 16% | 56% | 24%

## Slide 11: Survey Results
% of responders who observed corrosion by resistance type:
 | us/al | sm | n/an
Electrogalvanized | 23% | 43% | 28%
Hot dip galvanized | 9% | 40% | 46%
Non-ferrous | 15% | 31% | 36%
Stainless steel | 2% | 13% | 81%

## Slide 12: Survey Results
% of responders who observed corrosion by installation age:
 | us/al | sm | n/an
Less than 5 yrs old | 6% | 33% | 47%
5-10 yrs old | 29% | 53% | 16%
11-15 yrs old | 62% | 33% | 3%
More than 15 yrs old | 75% | 20% | 2%

## Slide 13: Survey Results
Is corrosion a significant issue with
 | YES | NO | No Opinion
Shingle fasteners | 37% | 46% | 17%
Tile fasteners | 27% | 45% | 28%
Ridge vent fasteners | 57% | 32% | 11%
Penetration fasteners | 47% | 40% | 13%
Other metal roof, screws, exposed | 18% | 82% | 

## Slide 14: Survey Results
Is corrosion a significant issue with
 | YES | NO | No Opinion
Electrogalvanized | 39% | 41% | 20%
Hot dip galvanized | 19% | 61% | 19%
Non-ferrous | 21% | 46% | 33%
Stainless steel | 7% | 83% | 10%

## Slide 15: Survey Results
Is corrosion a significant issue in
 | YES | NO | No Opinion
Coastal locations | 70% | 10% | 20%
Inland locations | 30% | 48% | 22%

## Slide 16: Survey Results
Do you check to see that fastener packages have the manufacturer's identifying marks and approved testing-agency labels for code compliance?
YES | 65%
NO | 10%
Sometimes | 25%

## Slide 17: Survey Results
Do the packages ACTUALLY have identifying marks and labels for code compliance?
  YES 54%
  NO 4%
  Sometimes 40% How often are they missing?
YES | 54%
NO | 4%
Sometimes | 40%
More than 10% missing | 29%
Less than 10% missing | 66%

## Slide 18: Survey Results
Have you noticed whether non-US manufactured products are more or less likely to have missing labels?
Non-US manufactured products are MORE likely to have missing labels | 41%
Non-US manufactured products are LESS likely to have missing labels | 6%
No Opinion | 51%

## Slide 19: Survey Results
Are Florida approved fasteners manufactured outside the U.S. more likely to show corrosion than a U.S. manufactured equivalent?
YES | 51%
NO | 9%
No Opinion | 39%

## Slide 20: Survey Results
Do you think that corrosion of metal roof fasteners is an issue the Florida Building Commission should seek additional remedies for?
YES | 38%
NO | 40%
No Opinion | 22%

## Slide 21: Discussion Points
Non-U.S. manufactured fasteners are less reliable
  Quality control issues
Electrogalvanized fastener corrosion is common
Corrosion in coastal applications is prevalent
Corrosion in inland applications is not uncommon
 The results indicates that further study is justified to seek a code modification

## Slide 22: Potential Solutions
Improved quality control for non-U.S. manufactured fasteners (who conducts ASTM A 90 ?)
Electrogalvanized fastener requirements
  Eliminate electrogalvanized fasteners
    Either entire state or coastal (boundaries to be determined)
    Alternative
  Increase requirement to ASTM A 641 class 2 (Table S1.1)
    Either entire state or coastal (boundaries to be determined)

## Slide 23: Additional Studies
Investigate the proposed electrogalvanized fastener requirements on previous slide
  Class 2 implications
    Cost issues
    Availability for roofing systems
    Ease of installation
    Effectiveness (will it actually improve long term performance?)
    Will this divert the market to non-ferrous and/or stainless?

## Slide 24: Additional Studies
Investigate the proposed electrogalvanized fastener requirements
  Define coastal boundary if isolating solution
    Literature is available for guidance (e.g. Fink, 1980)
  Effectiveness: Testing to evaluate performance of class 2 vs class 1
    TAS 114 Appendix E test protocol
    As-installed condition to replicate common installation related damage to zinc coating

## Slide 25: Additional Studies
Investigate the expansion of TAS 114 performance based requirement to the entire state (currently only HVHZ)
  Is TAS 114 performance based requirement an improvement on ASTM A 641 prescriptive requirement?
  Section 2.6.2 seems to indicate that ASTM A 641 class 1 electrogalvanized is the minimum performance requirement

## Slide 26: Questions / Discussion