(a) MATRIX OF CONCEPTUAL CHARACTERISTICS OF THE IECC AND THE FLORIDA ENERGY CODE

RESIDENTIAL ≤ 3 STORIES

|  | IECC 09 | FEECBC ’09 Supplement |
| --- | --- | --- |
| Characteristic | Prescriptive | Component Performance | Performance | Prescriptive | Performance |
|  |  |  |  | ‘09 |  | ‘09* |  |
| Building Envelope |  |  |  |  |  |
| Credit for reduced glass area? | no | no |  | no |  | no | yes |
| Penalty for increasing glass area? | no | partial |  | yes |  | yes | yes |
| Restricts glass area? | no | partial |  | no |  | yes | no |
| Credit for potential wall insulation levels? | no | partial |  | yes |  | no | yes |
| Credit for potential ceiling insulation levels? | no | partial |  | yes |  | no | yes |
| Credit for potential floor insulation level? | no | partial |  | yes |  | no | yes |
| Credit for air infiltration testing | yes | partial |  | yes |  | no | yes |
| Mechanical Systems |  |  |  |  |  |
| Credit for air conditioner efficiency? | no | no |  | no |  | no | yes |
| Credit for heating system efficiency? | no | no |  | no |  | no | yes |
| Credit for alternative water heating? | no | no |  | no |  | no | yes |
| Credit for tested ducts? | yes | no |  | yes |  | yes | yes |
| Penalty for untested ducts? | yes | yes |  | yes |  | no | possible |
| Lighting Systems |  |  |  |  |  |
| Considers alternative lighting? | yes | yes |  | no |  | no | no |
| General |  |  |  |  |  |
| Credit for solar, passive systems? | no | no |  | yes |  | no | yes |
| Equivalent stringency prescriptive vs performance? | no | no |  | no |  | yes | yes |
| Equivalent stringency for different fuel types? | yes | yes |  | no |  | yes | yes |

*Criteria are somewhat different for renovations, equipment change-outs and small additions.

COMMERCIAL and RESIDENTIAL > 3 STORIES

|  | IECC ‘09 | FEECBC ’09 Supplement |
| --- | --- | --- |
| CHARACTERISTIC | Prescriptive IECC ASHRAE 90.1 5.5 | Bldg Envelope Tradeoff ASHRAE 90.1 5.6 | Performance IECC 506 / ASHRAE 90.1 Chapter 11 | Prescriptive** | Performance ASHRAE 90.1 Chapter 11 |
| Building Envelope |  |  |  |  |  |
| Credit for reduced glass area? | No | No | No | --- | No |
| Penalty for increase glass area? | No | Yes | Yes | --- | Yes |
| Restricts glass area? | Yes | No | No | --- | No |
| Credit for potential wall insulation levels? | No | Yes | Yes | --- | Yes |
| Credit for potential ceiling insulation levels? | No | Yes | Yes | --- | Yes |
| Credit for potential floor insulation level? | No | Yes | Yes | --- | Yes |
| Credit for air infiltration testing? | No | No | No |  | No |
| Mechanical Systems |  |  |  |  |  |
| Credit for air conditioner efficiency? | No | No | Yes | --- | Yes |
| Credit for heating system efficiency? | No | No | Yes | --- | Yes |
| Credit for alternative water heating? | No | No | No | --- | No |
| Credit for tested ducts? | No | No | No | --- | No |
| Penalty for untested ducts? | No | No | No | --- | No |
| Lighting Systems |  |  |  |  |  |
| Credit for alternative lighting? | No | No | Yes | --- | Yes |
| General |  |  |  |  |  |
| Credit for solar, passive systems? | No | No | No | --- | No |
| Equivalent stringency prescriptive vs performance? | No | Yes | No | --- | No |
| Equivalent stringency for different fuel types? | Yes | No | Yes | --- | Yes |

**There are prescriptive criteria for shell buildings at first permit, renovations, equipment and lighting change-outs, and changes of occupancy type