## Slide 1
FBC Energy and Mechanical Technical Advisory Committees Concurrent Teleconference Meeting
June 20, 2017
Improved Hot Water Code Calculation
Final Report

## Slide 2: Research Purpose and Goal
Characterize hot water waste sources
Characterize implications of climatic differences on hot water use
Characterize energy impacts of hot water recirculation systems and controls with respect to energy consumption in Florida homes
Recommend Florida-specific methods to employ in the Florida Energy Code for residential hot water use and energy consumption calculations

## Slide 3
Project report will include recommendations suitable for consideration by the FBC in determining the most appropriate Florida-specific methods, procedure and calculation for determining the energy use effectiveness of domestic hot water systems for the residential FEC.
Expected Outcome and Impact
on the Code

## Slide 4
Four project tasks:
  Task 1: A “hot water” and “energy” search terms literature review
  Task 2: Development of hot water energy use calculation procedures by month, climate, circulation design and hot water system type
Research Approach

## Slide 5
Four project tasks (cont.):
  Task 3: Compare hot water energy use for 2, 3, and 4-bedroom homes in Miami, Orlando and Jacksonville calculated with new procedures vs. use determined by old (current) code calculation
  Task 4: Using EnergyGauge® USA simulations, determine and document the difference in overall energy code performance scores (total e-Ratios) for two sample homes.
Research Approach

## Slide 6
Searched on "hot water distribution" and "energy" terms in NREL, LBNL, ASHRAE and DOE BA databases + general search + other
40+ pertinent documents identified
Review showed anticipated levels of waste and use factors– including plumbing design, insulation, climate (time of year and location) and occupant demographics
Final report includes expanded summary discussion
Task 1: Literature Review

## Slide 7: Task 1: Literature Review
Principal factors not adequately considered by standard building energy code hot water calculations:
  Variation in service water temperatures by climate location
  Hot water system design significantly impacts both the quantity of hot water used and energy consumption
  Hot water circulation pumps can reduce hot water use but also dramatically increase energy use

## Slide 8
Starting point was industry vetted ANSI/RESNET 301-2014 Addendum A-2015
Florida-specific adaptations include:
  Calculation by month
  Florida climate adjustment (Tmains and Fmix)
Task 2: Calculation Procedure Development

## Slide 9
Starting point was industry vetted ANSI/RESNET 301-2014 Addendum A-2015
Florida-specific adaptations include:
  Calculation by month
  Florida climate adjustment (Tmains and Fmix)
Solar and HRUs addressed “upstream”
Task 2: Calculation Procedure Development

## Slide 10
Additional DHW characteristics accounted for by the new calculation procedure:
Recirculation DHW distribution systems
Pipe insulation
Fixture flow efficiency (standard or “low-flow”)
Pipe length
Drain water heat recovery (DWHR).
Task 2: Calculation Procedure Development (cont.)

## Slide 11
Interactive DHW Energy Consumption Calculator

## Slide 12
Draft Proposed Code Change Language

## Slide 13
DHW energy consumption calculator used to compare estimated annual hot water energy use of sample houses using the old (current) calculation procedure with the energy use resulting from using the new calculation procedure
Task 3: Energy Use Comparison

## Slide 14
Comparison used 2, 3 and 4 bedroom, 2,000 sq. ft., one-story sample houses with baseline efficiency electric water heaters in three Florida cities: Miami, Orlando and Jacksonville.
Task 3: Energy Use Comparison (cont.)

## Slide 15
Task 3: Energy Use Comparison (cont.)

## Slide 16
Task 3: Energy Use Comparison (cont.)

## Slide 17
EnergyGauge USA used to compare overall energy code performance scores (e-Ratios) using old (current) code hot water calculation procedure vs. new procedure
Comparison started with all-electric “near-code” sample house with standard hot water distribution system modeled in Miami, Orlando and Jacksonville
Task 4: Energy Code Performance Score Comparison

## Slide 18
Near-code house plus eight hot water distribution design and equipment efficiency variation cases:
  1) Near-code sample house with standard hot water distribution system
  2) Recirculation system with manual control and R-3 pipe insulation (manually controlled on/off, 178.89 ft. loop length, 10 ft. branch length and 50 Watt pump)
  3) Drain water heat recovery (DWHR); no other changes from Case #1
  4) Recirculation with manual control and 50% pipe length and pump power, and R-3 pipe insulation
  5) Same as Case #4 plus DWHR and low-flow fixtures
  6) Heat pump water heater (HPWH) with EF = 2.5; no other changes from Case #1
  7) Tankless natural gas water heater with EF = 0.83; no other changes from Case #1
  8) Recirculation with temperature control (instead of manual control) and R-3 pipe insulation
  9) Standard distribution system with 50% pipe length and R-3 pipe insulation.
Task 4: Energy Code Performance Score Comparison (cont.)

## Slide 19
Combined (cooling, heating and water heating) results for 2, 3 and 4 bedroom homes in the three cities are shown in report Table 4:
  e-Ratio differences between old (current) and new procedure for distribution design and conservation measures ranged from -6.55 to +11.42
  e-Ratio differences between old (current) and new procedure for EF = 0.83 tankless gas WH and EF = 2.5 HPWH ranged from +0.45 to +1.98 (reflects smaller overall e-Ratio impact from hot water in new procedure)
Task 4: Energy Code Performance Score Comparison (cont.)

## Slide 20
Task 4: Energy Code Performance Score Comparison (cont.)

## Slide 21
Mandatory circulation system control requirements in 6th Edition Section R403.5.1.1 are not explicit
Section R403.5.2 provides requirements for demand recirculation system control based on “receiving a signal from the action of a user of a fixture or appliance” and limiting the temperature of water entering cold piping
Refer to Section R403.5.2 in Section R403.5.1.1.
Controls for Recirculation Systems

## Slide 22
Recommendations
Since the hot water factors discussed can significantly affect residential energy use and are accounted for in the new Florida calculation procedure, we recommend adoption of the corresponding draft DHW code change language.

## Slide 23
Recommendations
Since the mandatory circulation system control requirements in Section R403.5.1.1 are not explicit, we recommend referring to Section R403.5.2 in Section R403.5.1.1 to insure that proper pump controls are required by the code.